## Slide 1: B3M38DIT1 Fault detection of sensors with machine learning using LSTM neural networks
Vít Zeman 09.01.2023

## Slide 2: Task
Fault detection on temperature sensor
Long-term time series data from multiple sensors
Using Long short-term memory (LSTM) neural network

## Slide 3: Faults
Three types of faults:
Drift:
  Linear
  ± [0.75; 1.25] kelvins every 5 days
Offset:
  Shift in temperature values
  ± [0.5; 5] Kelvin
Outliers:
  Sudden big jump in value
  ± [10; 30] Kelvin from average

## Slide 4: Data
Temperature, relative humidity, energy consumption and generation
Approx. 704 days of continuous measurements
Average over hour
Inconsistencies (-6999 °F, missing data)

## Slide 5: Dataset generation
Conversion to Kelvins
Random location and duration
4 classes
  Faultless
  Drift
  Offset
  Outlier
Distribution of [0.4, 0.2,0.2,0.2]

## Slide 6: RNNs and LSTMs
Memory: Previous input/output impacts current case
RNNs
  Only short memory
  Vanishing or exploding gradient
LSTMs
  Added long term memory
  Used for classification and prediction
Images: https://colah.github.io/posts/2015-08-Understanding-LSTMs/

## Slide 7: Proposed model
Idea use LSTM to extract features
Use Dense layers to classify outputs
Metrics
  Accuracy
  Confusion matrix

## Slide 8: Results
Accuracy 64%

## Slide 9: References
[1] S. Hochreiter and J. Schmidhuber. Long short-term memory. Neural computation, 9:1735–80, 12 1997.
[2] R. C. Staudemeyer and E. R. Morris. Understanding lstm-a tutorial into long short-term memory recurrent neural networks. 2019.